## Slide 1: FINAL PROJECT PRESENTATION
Image Processing Platform on the Zedboard Using the OV7670 Camera Pmod
FNU Hardik

## Slide 2
2
Presentation Outline
General Overview of Project
Required Tools
VHDL & IP files hierarchy
Top level RTL Schematic
Deeper look into OV7670 Pmod
Clocking Module (IP)
BRAM Module (IP)
Data Capture Module
Debounce (Restart) Module
Pmod Controller Module (SCCB & Register Settings)
VGA Output Module
Core Module
Pin Mappings
Video Demo
Limitations & Future Work

## Slide 3
3
General Overview of Project
The main aim of my project is to pipe the output of the peripheral camera module to any monitor accepting a VGA input.
This project is going to be focusing on a few aspects of this process, namely: the requirements to initiate the peripheral camera module, Programmable Logic modules necessary for implementation, external connections involved alongside their pin mappings and using BRAM’s to act as buffer modules.
Basic Block Diagram

## Slide 4
4
This Zynq chip is based on the ARM SoC architecture, but in this project, I don’t use the ARM functionality and limit myself to working only with the Programmable Logic part.
The camera module OV7670 is set to a resolution of 640x480, such a modest resolution is chosen because the Pmod itself is limited to a max resolution of 640x480.
The resulting video is sent out via the VGA cable at a speed of 25 frames per second, and output can be viewed on any monitor screen.
Basic Schematic for Implementation
General Overview of Project

## Slide 5
5
Tools Required
Micro USB cable: This will be connected to the PROG connector of the Zedboard and is needed to load the fabric logic as we’ll move forward.
Zedboard: Development board procured via the department of Electrical Engineering at CSUN. It is a convenient, well documented board that runs an ARM processor for managing the PS side.
OV7670 pmod: This is the Camera module utilized for the project
Connecting cables: Simple cables to connect the OV7670 camera unit
to the board interfaces of JA and JB.
VGA cable: This will carry the output to Its destination.
Monitor: This will be needed to view the final output.
Vivado IDE: Needs no introduction by now.
Digilent Zedboard Zynq-7000
OV7670 Camera

## Slide 6
VHDL & IP files hierarchy
6
The image on the left depicts the hierarchy of the design files involved in my project.
Things to note here:
IPs used in my project: Clocking Wizard, BRAM.
Controller module consists of two internal modules: i2c_sender and ov7670_registers.
Source files hierarchy

## Slide 7
Top-Level RTL Schematic
7
RTL Schematic for Implementation

## Slide 8
8
Deeper Look into OV7670 Pmod
My guide for this project was the reference manual for the Pmod: OV7670/OV7171 CMOS VGA (640x480) CameraChip Implementation Guide [2].
Functional Block Diagram: OV7670 Camera
Things to note in the block diagram:
Video Timing Generator: takes an input XCLK – which comes from my clk_wiz_3 (50Mhz) and generates PCLK among others as outputs. PCLK will inform our system of the rate at which data will arrive from the Pmod and can be scaled via register settings.
Registers: The set of registers needs to be initialized and be set according to a preset standard depending on what mode of output you want to implement.

## Slide 9
Clocking Module
9
Output Settings for Clocking Wizard IP
For providing a clock to my synchronous components I utilized the IP: Clocking Wizard.
But this IP does not generate a clock signal from nothing, it still requires an input clock which it will then modify into our requirements.
Possible clock sources on Zedboard: ZYNQ7 Processing System IP block or An on-board 100 MHz oscillator (IC17, Fox 767-100-136) which supplies the PL subsystem clock input on bank 13, pin Y9
We use two clocking frequencies in our design 25 Mhz and 50 Mhz.

## Slide 10
Block RAM Modules
10
Position of BRAM blocks in RTL Schematic
Port Settings for BRAM IP
Used as frame buffers in my design to store image pixel data.
BRAM 1 is 8 bits deep while BRAM 2 is 4 bits deep.
Port Depth is dictated by the target resolution.

## Slide 11
Data Capture Module
11
Schematic for Capture Logic Block
Captures the pixels coming from the OV7670 camera and stores them in our Block RAM.
Our Pmod is operating in YUV mode (Method of Initializing Pmod in this mode discussed later).
This module has two main states of operation:
  In this state it passes the data coming from the Pmod to the BRAM while assigning that data a unique address at which it will be stores inside the RAM module.
  In this state it disables the BRAM and increments the address channel to ensure that the next stream of inbound data will be assigned the proper address.
Clock frequency for this module is dependent on what the Pmod provides via OV7670_PCLK, this affects our design in two major ways:
  The BRAM module storing the frame pixel data will have to be clocked at the same speed to avoid data loss.
  This clk frequency will decide the upper fps limit of our final output, max fps possible will be half of this frequency. If we drive our output any faster, we’ll face data loss.

## Slide 12
Debounce (Restart) Module
12
This module has one simple function: program the chosen push button to generate one output per push irrespective of any clocking frequency, which can be used as a Restart for our system.
The btn is also connected to one of the on-board LED’s so we can confirm functionality.
Schematic for Debounce Block
VHDL – Debounce Module
The image on the right depicts how this behavior is achieved via VHDL.

## Slide 13
Pmod Controller Module
13
Internal RTL Schematic for Controller Module
This module is the main controller for the OV7670 Camera Pmod.
The basic purpose of this module is to provide the OV7670 Camera Chip with the necessary initialization settings so it may function as we intended.
Normally the initialization stage is something that we’re used to doing at the software stage in Vitis using C: turning ON the device, resetting it, calibrating it to specifics. But I chose to do this via VHDL because this Pmod uses SCCB Communication Protocol to talk to the outside world.
Although SCCB is similar to i2C it is not the same, which means I wouldn’t be able to utilize any function libraries pertaining to i2C communications.
Register data and addresses are concatenated together along with other preset elements and sent in a serial manner.

## Slide 14
Controller: Registers Module
14
The main function of this module is to provide the Pmod with the required data in order to initialize it in YUV mode.
All settings required for initialization can be found in the Pmod reference manual.
Register Settings for Initialization

## Slide 15
Controller: SCCB Communication Module
15
This is a modified 2-wire version of the original 3-wire SCCB protocol, 1:1 communication protocol [3-4].
SIO_C: this is a single-directional, active-low, control signal that must be driven by a master device. It indicates each transmitted bit. The master must drive SIO_C at logical 1 when the bus is idle. A data transmission starts when SIO_C is driven at logical 0 after the start of transmission.
SIO_D: this is a bi-directional data signal that can be driven by either master or slave devices. It remains floating, or tri-state when the bus is idle. Maintenance of the signal is the responsibility of both the master and slave devices in order to avoid propagating an unknown bus state.
2-wire SCCB Functional Block Diagram
Register Settings for Initialization

## Slide 16
VGA Output Module
16
Main purpose of this module is to generate analog 620x480 VGA Output.
This module is simply scanning the pixel data from the BRAM modules and placing the same data onto vga red, blue and green output cables.
The reason for placing the same data onto all three red, blue and green channels is because after coming out of the core module in my design my frame_pixel data is already in grayscale format.
VGA Connections on the Zedboard
Schematic for VGA Module
VGA Port

## Slide 17
Core Module
17
The basic purpose of this module is to convert color data to grayscale.
The need for this module arose because initially I was setting the OV7670 Camera to initialize in an RGB format and realizing grayscale from RGB is complicated.
To convert Grayscale from RGB, the formulae is: Grayscale = 0.299R + 0.587G + 0.114B
Is there a better way … 🤔
Schematic for Core Module

## Slide 18
Core Module
18
The basic purpose of this module is to convert color data to grayscale.
The need for this module arose because initially I was setting the OV7670 Camera to initialize in an RGB format and realizing grayscale from RGB is complicated.
To convert Grayscale from RGB, the formulae is: Grayscale = 0.299R + 0.587G + 0.114B
Is there a better way … 🤔
YUV format !!!
Y(Luminance) U(Blue-luminance) V(Red-luminance)
To convert Grayscale from YUV, the formulae is: Grayscale = Y
According to our initialization settings we set YUV in a 4:2:2 format, meaning bits 7-4 are assigned to Y, 3-2 are assigned U and 1-0 are assigned V.
This works perfectly for us as we needed a 4-bit format for the VGA output anyways.
Now we can just connect our output to the 4 MSB bits from the incoming data and we’ll have grayscale frame pixel data.
Schematic for Core Module

## Slide 19
19
Pin Mappings
Pin mappings for all external connections involved in design
The images below depict all pin mappings involved in my design.
Mostly external connections involving Pmod and VGA.
Few internal connections involving on-board LEDs for indication purposes.

## Slide 20
20
Video Demo
Sample Output Image
Fps check: https://youtu.be/34jz1RZQFFE

## Slide 21
21
Limitations & Future Work
Limitations:
Project is in grayscale because I couldn’t crack the mysteries behind color video processing. Images on the right-hand side show my failed attempts.
Future Work:
Fine-tuning and trying to perfect a color implementation.
The core module is placed in an ideal place where we can think about adding certain logic for computer vision algorithm and we can easily add additional RAM modules to help in this data processing.
Failed attempt 2
Failed attempt 1

## Slide 22
22
References
[1] https://www.xilinx.com/content/xilinx/en/support/university/boards-portfolio/xup-boards/DigilentZedBoard/_jcr_content/root/parsys/xilinxcolumns_f62b/childParsys-0/xilinxbuybox_943e/thumbnail/image.img.jpg/1381869368208.jpg
[2]http://www.haoyuelectronics.com/Attachment/OV7670%20+%20AL422B%28FIFO%29%20Camera%20Module%28V2.0%29/OV7670%20Implementation%20Guide%20%28V1.0%29.pdf
[3] https://www.waveshare.com/w/upload/1/14/OmniVision_Technologies_Seril_Camera_Control_Bus%28SCCB%29_Specification.pdf
[4] http://www4.cs.umanitoba.ca/~jacky/Teaching/Courses/74.795-LocalVision/ReadingList/ov-sccb.pdf

## Slide 23
Q&A